## Slide 1: Smartphone app for non-invasive detection of anemia using only patient-sourced photos
Link to paper

## Slide 2: AIM Cons of clinical assessment of Anemia Why fingernail?
To demonstrate a system in which accurate Hgb measurements are obtained with a smartphone without the need for any external equipment
The gold standard CBC Hgb level measurement requires:
blood sampling by a trained phlebotomist,
a clinical hematology analyzer with the required electrical power,
biochemical reagents, and
infrastructure thereof, along with a trained laboratory technician to perform the analysis,
all of which are especially problematic in rural and low-resource settings, where anemia is most prevalent
fingernails are straightforward for a user to self-image, unlike conjunctiva, and also have low person-to-person size and shape variability, unlike palmar creases

## Slide 3: Methodology Dataset and Testing
Fingernail data, skin color data, and image metadata were extracted from fingernail bed smartphone images via MATLAB (Mathworks, Natick, MA)
Regions of interest, from which fingernail and skin color data were extracted, were manually selected to ensure that fingernail irregularities were excluded from analysis
Color data were extracted from each region and averaged together across fingers for each subject
An algorithm was then written in MATLAB utilizing robust multi-linear regression with a bisquare weighting algorithm to relate the image parameter data to CBC Hgb levels for each patient
To develop the algorithm as a tool to screen for anemia, the entire study population (337 subjects) was randomly split into a discovery group (237 subjects) and a testing group (100 subjects)
Validation was performed by applying the smartphone algorithm to each testing image and comparing the algorithm generated Hgb result with the CBC Hgb result
This process was repeated 1000 times with different, randomly-selected without replacement, discovery/testing groups to minimize residual error, thereby optimizing the parameters of the algorithm for anemia screening