## Slide 1: Detecting Clinical Signs of Anaemia From Digital Images of the Palpebral Conjunctiva
- By Giovanni Dimauro, Attilio Guarini, Danilo Caivano, Francesco Girardi, Crescenza Pasciolla, And Angela Iacobazzi
A presentation by Shrey Gupta

## Slide 2: Introduction
Anemia is a condition where the body does not have enough healthy red blood cells to carry sufficient oxygen to the body's tissues
Anemia is typically diagnosed through blood tests to measure the levels of hemoglobin, hematocrit, and red blood cells
Traditional methods of anemia diagnosis can be invasive, costly, and require specialized equipment and trained medical professionals. In some cases, traditional methods may also be unavailable or impractical in certain settings
The paper discusses a novel method of diagnosing anemia using digital images of the palpebral conjunctiva, which is a non-invasive and cost-effective alternative to traditional methods of diagnosis

## Slide 3: Related Work
Digital image processing has been used to investigate the relationship between the pallor of fingertips and the concentration of hemoglobin in the blood.
HemaApp is an application for monitoring hemoglobin levels based on the method described above with the innovative use of different artificial light sources.
Another approach is based on the redness of the palpebral conjunctiva. To identify the image margins of the palpebral conjunctiva, an edge detector algorithm was used with the addition of a Gaussian filter
This study takes into consideration 102 people, with new features, new algorithms for extracting color characteristics, a method for assisted selection of the area of the palpebral conjunctiva, and experimentation with oversampling of the dataset with the SMOTE and ROSE algorithms to balance the anemic and non-anemic samples.

## Slide 4: Dataset
The anaemia alarm condition is based on a 2-class evaluation principle: the patient’s condition is marked as ‘risk’ when Hb<11.5 g/dl and ‘safe’ when Hb>=11.5
The experiments were carried on 102 persons (25 persons with Hb <11.5 gm/dL)
Dataset Balancing Problems
  In this work, two algorithms for class balancing are studied in the case of safe and risk classes related to anemia: Random Over-Sampling Examples (ROSE) and Synthetic Minority Over-sampling Technique (SMOTE).
  ROSE creates new artificial data through a smoothed bootstrap-based technique, while SMOTE creates synthetic samples to oversample the minority class.
  SMOTE leaves the original data in the dataset, while ROSE leaves no data in the original state.

## Slide 5: Diagnostic Support
The palpebral conjunctiva is a suitable site for anaemia observation due to high vascularization.
A low-cost, user-friendly medical device is developed for home use, consisting of a smartphone, macro-lens, and special spacer.
The device takes high-resolution photos of the conjunctiva and is insensitive to ambient light.
The software system enables anaemia monitoring and direct medical consultation, with data sent to physicians immediately.
The acquisition process involves taking a photo of the orbital region and segmenting it using the SLIC Superpixels algorithm.
The macro-regions of pixels make it easy to select the region of interest for feature extraction

## Slide 6: Image Analysis And Feature Extraction
Hemoglobin's absorption characteristics give it its typical color and reflect red light while absorbing green light.
Erythematous index (EI) and component a∗ of the CIE-Lab color space are used to quantify paleness.
The EI is calculated based on the reflection of red and green light, with higher amounts of haemoglobin reflecting more red light and less green light.
Component a∗ of the CIE-Lab color space is used to estimate changes in color perception, with increasing a∗ values indicating increasing redness of the conjunctiva.
Color analysis can provide an objective and quantifiable assessment of skin reactions to allergy tests and other medical conditions.
Image standardization was unnecessary due to the use of a single smartphone and controlled ambient lighting conditions.

## Slide 7: COLOUR CLUSTERING
K-means algorithm used to choose prevalent colours
RGB colour space used to represent pixels in a 3D space
Euclidean distances calculated between points to assign significant centroids
Denser areas of the image form partitions with centroids representing prevailing colours
Number of tones selected by algorithm equivalent to parameter 'K'
Too low K value results in considerable approximation, too high K value makes it difficult to identify distinct clusters
Based on dataset experiences, images of palpebral conjunctiva contain on average 10 significant colours for feature extraction.

## Slide 8: MANUAL SEGMENTATION OF THE PALPEBRAL CONJUNCTIVA
Two unbalanced datasets were used for training the classification algorithms.
10-fold-stratified-cross-validation technique was used for testing the efficiency of prediction models.
All classifiers showed high error rates and a probability of no alarm greater than zero.
SMOTE and ROSE balancing algorithms were applied to balance the datasets.
SMOTE-balanced dataset: kNN algorithm showed the best performance with no false negatives.
ROSE-balanced dataset: kNN algorithm showed the best performance with no false negatives.
Conclusion:
  Dataset balancing improves the performance of classification algorithms in identifying conjunctives, with the kNN algorithm being the best performing algorithm in both SMOTE and ROSE balanced datasets.

## Slide 9: ASSISTED SEGMENTATION OF THE PALPEBRAL CONJUNCTIVA
Image segmentation of palpebral conjunctiva was done using superpixels
Aim is to develop a free tool for anemia detection usable by patients and specialized personnel
kNN classifier with features a* and EI showed reliable evaluation of anemia suspicion
ROSE balancing algorithm was more effective than SMOTE algorithm in reducing failure to alarm probability to zero
Dataset balancing achieved zero false negatives, acceptable to avoid misleading results
No customization done for patient characteristics; improvement possible by considering gender and age thresholds for anemia
Photographs taken without strict instructions to simulate real use

## Slide 10: Conclusion
Non-invasive method to monitor and identify potential risk of anemia
System detects clinical signs of anemia from digital images of palpebral conjunctiva
New acquisition device (spacer and lens) is inexpensive and simple to use
Absence of ambient light in acquisitions is fundamental, making preventive standardization processes unnecessary
Color clustering applied to images allows abstraction from irrelevant details
Appropriately balanced dataset allows better estimation of relationship between pathology and conjunctival pallor
Implementation of classifier for two risk classes supports end users
Results guarantee reliability of system as personal monitoring tool
System could considerably reduce number of candidate subjects for blood sampling, highlight suspected anemic state of persons at risk (e.g. 9-12 year old girls who experience menarche), and help with massive screening in resource-poor settings, especially in rural areas.

## Slide 11: Thank You