## Slide 1: Novel Biased Normalized Cuts Approach for the Automatic Segmentation of the Conjunctiva
- By Giovanni Dimauro, and Lorenzo Simone
A presentation by Shrey Gupta

## Slide 2: Introduction
Anemia: blood disorder causing deficiency in red blood cells, impairing oxygen transport to tissues and organs.
Erythrocyte production involves bone marrow and erythropoietin, a hormone produced by kidneys.
Hemoglobin: iron-containing protein in erythrocytes, transports oxygen from lungs to tissues.
Diagnosis: complete blood count (CBC) to check hemoglobin and hematocrit levels.
WHO developed hemoglobin color scale (HCS) for simple, cheap, and robust hemoglobin measurement.

## Slide 3: Haemoglobin Spectrophotometry
HCS and physical examination of exposed tissues rely on color perception, but a chemical insight is required to analyze and handle this from a computer vision perspective.
Spectrophotometry in chemistry is used to measure the reflective or absorption properties of a material from a wavelength perspective. Hemoglobin spectra vary depending on whether it is bound to oxygen, carbon monoxide or nothing (deoxygenated Hb).
Palpebral conjunctiva has been a good spot for anemia diagnosis due to its highly vascular area. A multi-layered tissue model approximates the lower eyelid with seven layers, allowing for digital image domain approximations.
Hb and HbO2 both absorb wavelengths from 275 to about 550 nm corresponding to a visible spectrum from purple to light green. Each frequency above 600 nm is highly reflected, matching with colors from orange to dark red.
The cytoplasm of the red blood cell is rich in hemoglobin, responsible for the reddish appearance of exposed tissues and blood. Digital image analysis related to hemoglobin is accomplished through segmentation and laboratory-based experiments

## Slide 4: Related Works
Researchers have worked on non-invasive methods for anemia detection through hemoglobin estimation.
Conjunctiva hue has been tested for anemia evaluation, with mixed results depending on the objective of the assessment and training of field personnel.
Digital photography using machine learning and automatic segmentation procedures has shown promising results in minimizing variance and optimizing specificity and sensitivity.
Smartphone-based applications have been developed for monitoring blood hemoglobin concentration using chromatic analysis of digital images of fingernail beds or a light source pointed to the patient's finger.
Color features from hemoglobin reflectance spectrum play a key role in biasing towards a region of interest proposal.
Few works in literature deal with automatic segmentation of the conjunctiva, with varying levels of reliability compared to manual segmentation by an expert physician

## Slide 5: Proposed Method
Digital images from the dataset are converted into an RGB color space matrix representation
Segmentation process has three phases: clustering approach for dimensionality reduction, grouping as graph partitioning, and final ROI extraction
Preliminary clustering step speeds up N-Cuts performance
Region adjacency graph (RAG) groups pixels together based on spatial and color differences
A non-linear relation between brightness intensities from red and green channels is aimed to be established
Assumptions of reflectance rate by a spectrophotometry point of view are taken into account

## Slide 6: Results
The study involves capturing digital images of patients' eyes using a device assembled on a Samsung S6 smartphone.
94 patients participated in the study, with ages ranging from 19 to 75 (average 34) and a roughly equal gender distribution.
Each image was manually cropped to isolate regions of interest (the palpebral and forniceal conjunctiva) for comparison with the automated segmentation output.
Spatial and color metrics were evaluated to assess the quality of the segmentation, with F1 (Sørensen-Dice coefficient) and accuracy being the most useful.
The results indicated that the segmentation algorithm was effective, with high values for specificity and reasonable sensitivity/F1.

## Slide 7: Results
CIELAB is a color space used for erythema analysis and computer vision in diagnostics, with a* having a well-known correlation with hemoglobin values.
The study examined the strength of linear correlation between mean a* values extracted from digital images of conjunctivas and the relative Hb g/dL concentration from blood samples taken almost at the same time of picture capturing phase.
The Pearson correlation coefficient was used to estimate the weight of linear correlation between the two standardized vectors, with values of 0.59 and 0.53 obtained for manual and automated segmentation, respectively.
These results suggest a moderate linear correlation between a* values and Hb concentration, as well as a robust contiguity between manual and automated segmentation. Further investigation of color properties in left-out or added regions could be interesting.

## Slide 8: Conclusion
Developed an automated segmentation procedure for conjunctival regions using graph partitioning
Maximized correlation between color properties and hemoglobin concentration in blood
ROIs were compared to ground truth using state of the art metrics for similarity and PCC
Results showed reliability and capability of generalizing to patients of heterogeneous classes
Proposed method can pave the way for further studies on anemia diagnosis support
Advancement provides non-invasive image capturing procedure for wearable devices screening Hb risk category in real-time without physician support

## Slide 9: Thank You